## Slide 1
NICCI
Network-Informed Control – Control-Informed network
Meeting in Aachen 2017
Wireless Cell
RRM
Markus Kögel, Rolf Findeisen

## Slide 2: Network aware control Evaluating limits of achievable performance (MD group)
  Setup
  dynamics
    unknown, but bounded uncertainties
    discrete, time linear dynamics
    noisy measurements
    network
    ideal communication no loss/no (significant) delay (or compensated – data sent arrives before next time instant)
    here: one link to sensors/actuators (extension straightforward)
  Question – controller optimizes communication for performance ►determine when/what/where to send for optimal performance
Challenge: when/what/where to send to optimize control performance
Trade-offs: (example)
less latency or more data
  Core idea: exploit robust output feedback MPC

## Slide 3: Different communication choices possible (given by RRM)
what to communicate (how much data):
naïve choice: sensors send and controller actuators use backupif nothing new is received general case: multiple measurements/commands in each packet
  piggy back old measurements, e.g. send at k
  send input sequences, e.g. send at k
Possible when/where to communicate formulations
each time instant one communication from sensors or to actuators
on average 0.75 communications each time instant
yes
from sensors/ to actuators
Solution approach to optimize communication
consider fixed communication schedule tube
simple performance evaluation necessary + avoid influence of tuning

## Slide 4: Combination with robust output feedback MPC: basics
Framework
LTI system with bounded process noise
constraints on state and input
sensor measurements, bounded noise
Control objective:
worst case optimal set-point tracking
minimize back off from constraints (set – tune “tube controller”
  Robust output feedback MPC:
  tube approach: decompose dynamics into
  nominal system (no noise) + MPC
  error systems + fixed, linear controller
“economic” performance
real/tightened constraint
worst case bounds on/nominal dynamics
Contribution:
automated “optimal” controller design (for given communication schedule)
allows to compare different communication schedules
guarantees on closed loop behavior (constraint satisfaction, robust stability)
computationally efficient